## Slide 1
Reuse Methodology Manual for System-On-Chip Designs
Chapter 5: RTL Coding Guidelines
Notes: This is the light cover slide option.

## Slide 2: Chapter content
  Basic Coding Practices.
  Coding for Portability.
  Guidelines for Clocks and Resets.
  Coding for Synthesis.
  Partitioning for Synthesis.
  Designing with Memories.
  Code Profiling.

## Slide 3: 5.2 Basic Coding Practices
5.2.1 General Naming Conventions
Rule – Develop a naming convention for the design. Document it and use it consistently throughout the design.
Guideline – Use lowercase letters for all signal names, variable names, and port names.
Guideline – Use uppercase letters for names of constants and user-defined types.
Guideline –Use meaningful names for signals, ports, functions, and parameters. For example, do not use ra for a RAM address bus. Instead, use ram_addr.
Guideline – If your design uses several parameters, use short but descriptive names. During elaboration, the synthesis tool concatenates the module’s name, parameter names, and parameter values to form the design unit name. Thus, lengthy parameter names can cause excessively long design unit names when you elaborate the design with synthesis tools.

## Slide 4: 5.2 Basic Coding Practices
Guideline – Use a consistent name for the clock signal, such as clk. If there is more than one clock in the design, use clk as the prefix for all clock signals (for example, clkl, clk2, or clk_interface).
Guideline – Use the same name for all clock signals that are driven from the same source.
Guideline – For active-low signals, end the signal name with an underscore followed by a lowercase character (for example, _b or _n).Use the same lowercase character consistently to indicate active-low signals throughout the design.
Guideline – Use a consistent name for reset signals, such as rst. If the reset signal is active low, use a name like rst_n (or substitute n with whatever lowercase character you are using to indicate active-low signals).

## Slide 5: 5.2 Basic Coding Practices
5.2.1 General Naming Conventions
Rule – When describing multibit buses, use a consistent ordering of bits. For VHDL, use either (x downto 0) or (0 to x). For Verilog, use [x:0] or [0:x]. Using a consistent ordering helps improve the readability of the code and reduces the chance of accidently swapping order between connected buses.
Guideline – Use[x:0]for multibit signals in Verilog and (x downto 0) for multibit signals in VHDL. We make this recommendation to establish a standard, and thus achieve some consistency across multiple designs and design teams.
Guideline – When possible, use the same name or similar names for ports and signals that are connected (for example, a => a; or a => a_int;).

## Slide 6: 5.2 Basic Coding Practices
5.2.3 State Variable Names
Rule – Use a distinctive suffix for state variable names. Recommended names are <name>_cs for the current state, and <name>_ns for the next state.
5.2.4 Include Informational Headers in Source Files
Rule – Include a commented, informational header at the top of every source file, including scripts. The header must contain:
Legal statement: confidentiality, copyright, restrictions on reproduction.
Filename.
Author.
Description of function and list of key features of the module.
Date the file was created.
Modification history including date, name of modifier, and description of the change.

## Slide 7: 5.2 Basic Coding Practices

## Slide 8: 5.2 Basic Coding Practices
5.2.5 Use Comments
Rule – Use comments appropriately to explain processes, functions, and declarations of types and subtypes.
Comments should be placed logically, near the code that they describe.
Comments should be brief, concise, and explanatory.
Avoid “comment clutter”; obvious functionality does not need to be commented.
5.2.6 Keep Commands on Separate Lines
Rule – Use a separate line for each HDL statement. Although both VHDL and Verilog allow more than one statement per line, the code is more readable and maintainable if each statement or command is on a separate line.
5.2.7 Line Length Guideline – Keep the line length to 72 characters or less.

## Slide 9: 5.2 Basic Coding Practices
5.2.8 Indentation Rule – Use indentation to improve the readability of continued code lines and nested loops.
Guideline – Use indentation of 2 spaces. Larger indentation (for example, 8 spaces) restricts line length when there are several levels of nesting.
Guideline – Avoid using tabs. Differences in editors and user setups make the positioning of tabs unpredictable and can corrupt the intended indentation. There are programs available, including language-specific versions of emacs, that will replace tabs with spaces.

## Slide 10: 5.2 Basic Coding Practices

## Slide 11: 5.2 Basic Coding Practices
5.2.9 Do Not Use HDL Reserved Words
Rule – Do not use VHDL or Verilog reserved words for names of any elements in your RTL source files. Because macro designs must be translatable from VHDL to Verilog and from Verilog to VHDL, it is important not to use VHDL reserved words in Verilog code, and not to use Verilog reserved words in VHDL code.
5.2.10 Port Ordering
Rule– Declare ports in a logical order, and keep this order consistent throughout the design.
Guideline – Declare one port per line, with a comment following it (preferably on the same line).
Guideline – For each interface, declare the ports in the following order:

## Slide 12: 5.2 Basic Coding Practices
5.2.11 Port Maps and Generic Maps
Rule – Always use explicit mapping for ports and generics, using named association rather than positional association.

## Slide 13: 5.2 Basic Coding Practices
5.2.13 Use Functions
Guideline – Use functions, when possible, instead of repeating the same sections of code. If possible, generalize the function to make it reusable.
5.2.14 Use Loops and Arrays
Guideline – Use loops and arrays for improved readability of the source code. For example, describing a shift register, PN-sequence generator, or Johnson counter with a loop construct can greatly reduce the number of lines of source code while still retaining excellent readability.

## Slide 14: 5.2 Basic Coding Practices

## Slide 15: 5.2 Basic Coding Practices
Guideline – Arrays are significantly faster to simulate than for loops. To improve simulation performance, use vector operations on arrays rather than for loops whenever possible.

## Slide 16: 5.2 Basic Coding Practices
5.2.15 Use Meaningful Labels
Rule – Label each process block with a meaningful name. This is very helpful for debug. For example, you can set a breakpoint by referencing the process label.
Guideline – Label each process block <name>_PROC.
Rule – Label each instance with a meaningful name.
Guideline – Label each instance U_<name>.

## Slide 17: 5.3 Coding for Portability
5.3.2 Do Not Use Hard-Coded Numeric Values
Guideline – Use constants instead of hard-coded numeric values.
Using constants has the following advantages:
Constants are more intelligible as they associate a design intention with the value.
Constant values can be changed in one place.
Compilers can spot typos in constants but not in hard-coded values. For example, if MY_BUS_LENGTH is misspelled MY_BUS_LEGTH, the error will be flagged; however, if the intended value 0x100001 is given as 0x10001, the error will not be caught.

## Slide 18: 5.3 Coding for Portability

## Slide 19: 5.3 Coding for Portability
5.3.4 Constant Definition Files
Guideline – Keep constant and parameter definitions in one or a small number of files with names such as DesignName_constants.v or DesignName_parameters.v
  Source files should not make references to constant definition files with the include statement, since this will cause problems if the core is instantiated multiple times in the design, but with different constant values. We recommend that constant definition files be specified only on tool command lines.

## Slide 20: 5.3 Coding for Portability
5.3.5 Avoid Embedding Synthesis Commands
Although it is possible to embed synthesis commands directly in the source code, this practice is not recommended. Others who synthesize the code may not be aware of the hidden commands, which may cause their synthesis scripts to produce poor results. If the design is reused in a new application, the synthesis goals may be different, such as a higher-speed version
5.3.6 Use Technology-Independent Libraries
Guideline – For arithmetic components, use the DesignWare Foundation Library.
Guideline – Avoid instantiating gates in the design. Gate-level designs are very hard to read, and thus difficult to maintain and reuse. If technology-specific gates are used, then the design is not portable to other technologies.
Guideline – If you must use technology-specific gates, then isolate these gates in a separate module. This will make it easier to modify these gates as needed for different technologies.
Guideline – If you must instantiate a gate, use the Synopsys generic technology library, GTECH.

## Slide 21: 5.4 Guidelines for Clocks and Resets
5.4.1 Avoid Mixed Clock Edges
Guideline – Avoid using both positive-edge and negative-edge triggered flip-flops in your design.
Clocking on both edges creates several problems:
1) Timing closure becomes challenging.
2) Most scan-based testing methodologies require separate handling of positive and negative-edge triggered flops.
Rule – If you must use both positive-edge and negative-edge triggered flip-flops in your design, be sure to model the worst-case duty cycle of the clock accurately in synthesis and timing analysis.
Guideline – If you must use a large number of both positive-edge and negative-edge triggered flip-flops in your design, it may be useful to separate them into different modules. This makes it easier to identify the negative-edge flops, and thus to put them in different scan chains.

## Slide 22: 5.4 Guidelines for Clocks and Resets
5.4.2 Avoid Clock Buffers
Guideline – Avoid hand instantiating clock buffers in RTL code. Clock buffers are normally inserted after synthesis as part of the physical design.
5.4.3 Avoid Gated Clocks
Guideline – Avoid coding gated clocks in your RTL because:
1) Improper timing of a gated clock can generate a false clock or glitch, causing a flip- flop to clock in the wrong data.
2) Gated clocks cause limited testability because the logic clocked by a gated clock cannot be made part of a scan chain.

## Slide 23: 5.4 Guidelines for Clocks and Resets
Integrated Clock Gating (ICG) Cell

## Slide 24: 5.4 Guidelines for Clocks and Resets

## Slide 25: 5.4 Guidelines for Clocks and Resets

## Slide 26: 5.4 Guidelines for Clocks and Resets

## Slide 27: 5.4 Guidelines for Clocks and Resets
5.4.4 Avoid Internally Generated Clocks
Guideline – Avoid using internally generated clocks in your design as they cause limited testability because logic driven by them cannot be made part of a scan chain.

## Slide 28: 5.4 Guidelines for Clocks and Resets
5.4.5 Gated Clocks and Low-Power Designs
Guideline – keep the clock and/or reset generation circuitry as a separate module at the top level of the design.

## Slide 29: 5.4 Guidelines for Clocks and Resets
5.4.6 Avoid Internally Generated Resets
Guideline – Avoid internally generated, conditional resets if possible. Generally, all the registers in the macro should be reset at the same time. If a conditional reset is required, create a separate signal for the reset signal, and isolate the conditional reset logic in a separate module.

## Slide 30: 5.4 Guidelines for Clocks and Resets
5.4.7 Reset Logic Function
Guideline – The only logic function for the reset signal should be a direct clear of all flip-flops. Never use the reset inputs of a flop to implement state machine functionality. Reserving reset pins on flops for reset only makes it easier to generate buffer trees for resets.

## Slide 31: 5.4 Guidelines for Clocks and Resets
5.4.8 Single-Bit Synchronizer
Guideline – Use two flip-flop stages to transfer single bits between clock domains. To prevent transfer of glitches, do not connect combinatorial logic from one clock domain to another.
5.4.9 Multi-Bit Synchronizers
Guideline – Do not use multiple copies of a single-bit synchronizer between domains. Instead, use a reliable handshake circuit or multibit coding scheme such as Gray code.